Socket programming notes:

htons(port_number) converts port number to compatible with network
inet_addr(char *c) converts the IP string seperated by dots to compatible with network
atoi(char *) : string to integer.

htonl(char *IP): will convert char IP to unsigned long

you can use htons(int) for port number and htonl(char*) for IP

memset() or bzero() work same: assigns zero to address space of socket.

important note: port number and IP can be received as string, but needs to be converted in network compatible forms.

5. Implementation of echo client:
- client sends msg to server.
- Server will receive that msg
- Server will sent that msg to client again.
6. Understanding UDP sockets:
- no handshake like TCP
- once server gets request it keeps sending doesn’t care wheather data is received by client or not.
- Single packet transfer
- no error connection
- commonly used for broadcast
- sendto() and recvfrom() to send and receive operations
- It doesn’t need accept or connect like TCP
- programming:
- type of connection: SOCK_DGRAM
7. Remote Data Processing, Headers (TCP vs UDP):
- Raw data is sent to server by client/clients
- server will send processed data to client/clients
8. setting and retrievingsocket characteristics
- we can set and get the value of sockets
- socket type and socket error can only be retrieved and can bot be changed.